Sefton Adult Learning Service
Industrial and Machine control systems
Presented
By Tony McDonald
Class 2 Inputs and Outputs

---
Long-term Goal
All Computers must have Inputs and Outputs (I/O)
1. For any computer to be useful it must have Inputs and Outputs. Even if that is only a keypad and a screen! Modern computers have many input and output streams. On your phone these may include:
  - Keypad and screen.
  - USB ports.
  - Blue Tooth.
  - Serial ports.
  - Wi-Fi.
  - Near Field.
  - Transceiver.

---
Industrial Computers and PLC systems must have many more Inputs and Outputs (I/O)
1. For a control system there must be many inputs and outputs. These may include:
  - Keypad and screen.
  - USB ports.
  - Output Drivers (these are used to turn services on or off).
  - Digital inputs (these are used to sense events).
  - Serial ports.
  - Analogue outputs (these control motors etc.).
  - Analogue inputs (to measure temperature etc.).
  - Encoder inputs.

---
Customer Wishes
How computers see the world
1. Computers are devices that are digital (there are also analogue).
2. Computers use Binary Numbers, these are number to the base 2. It is important to understand binary and hexadecimal if you want to be a good programmer.
4. In decimal system the biggest single number you can have is 9, in binary the biggest number is 1. If we want to write a number bigger than 1 in binary we have to use multiple digits for example the number 2 decimal is written as 10. To prevent confusion binary numbers often have a lower case b written after them. For example 10 could be 10 or 2 in binary so binary is often written as 10b. As in all numeric bases the columns of the number are power of the base. Don’t worry there is no nasty maths yet!

---
How computers see the world Binary
8 bit Binary table
128	64	32	16	8	4	2	Units	Decimal
0	0	0	0	0	0	0	0	0
0	0	0	0	0	0	0	1	1
0	0	0	0	1	0	0	1	9

---
Fulfilling Customer Needs
Working Hexadecimal and Binary
1. From the table above you can see that in a binary system it could difficult to work only in decimal or Binary for that matter. For this reason programming systems include at least three numeric base systems, these are Binary, Decimal and hexadecimal. There are time where it is better to work in other base for example if we are working with inputs and outputs it is better to work with decimal or hexadecimal. For example if we think of a decimal number 127, in binary 01111111b. In hexadecimal it is 7F
3. Why use Hex?
4. Hexadecimal is to the base 16 so it is easy to think of the binary equivalent. Hex uses numbers 0 to 9 and the values is exactly the same as decimal 10+ uses A to F. For example 10 is A often hex has a 0x in front of it to show it is to the base 16 for example 0xA is 10 also some compilers use a dollar sign $A some use a trailing h for example Ah.

---
Working Hexadecimal and Binary
1. 8 bit Hexadecimal table:
8	4	2	u	8	4	2	u	Dec	Hex
128	64	32	16	8	4	2	u
0	0	0	0	0	0	0	0	0	00
0	0	0	0	0	0	0	1	1	01
0	0	0	0	0	0	1	0	2	02
0	0	0	0	1	1	1	1	15	0f
0	0	1	0	0	0	1	1	35	23

---
Working Hexadecimal and Binary
16 Bit Hexadecimal
8	4	2	U	8	4	2	U	8	4	2	U	8	4	2	U	HEX
32768	16384	8196	4096	2048	1024	512	256	128	64	32	16	8	4	2	U
0	0	0	0	0	0	0	0	0	0	0	0	1	0	0	0	0008
1	0	0	0	1	0	0	0	1	0	0	0	1	1	1	1	888F
1	1	1	1	0	0	0	0	0	0	0	0	1	0	0	0	F008
1	0	1	0	0	1	0	1	1	0	1	1	1	1	0	0	A5BC
																E987
																9875
																FEDC

---
Encoders and Sensors
Motion controllers rely on feedback to tell them the positioning of the servo system they control. This can be thought of in the same way as we use our eyes. Motion controllers rely on a technique which involves a command position, this is where the end-user requires a servo to move to. The actual or current position is given by the encoder. The motion controller uses a complex algorithm which involves a PID loop normally having at least five terms, but the basic algorithm can be thought of as position error multiplied by the gain. The system gain can be set by the end-user. The motor can be thought of like a spring and the gain is like the stiffness of the spring. The higher the gain the stiffer the spring. A motor can be thought of as a giant magnetic spring controlled by the motion controller. There are different types of encoders the most common of these are the incremental encoders these produce two main signals the A and the B channel. Some encoders have a Z pulse. This pulse is exactly one mechanical pulse wide and occurs once every revolution. An encoder can be either optical or magnetic. Optical encoders work by having a slotted disc through which infra-red light is shone. A phase plate is arranged so that light is interrupted by the disc. The phase plate has two channels which are organised to be 90° apart.

---
Optical encoders
- Please see an image of an encoder disk. Disk can be made from polymer, glass or metal (normally stainless steel).
- The image right lower shows the output of a typical increment encoder.

---
Absolute Rotary encoders
1. There are two main types of absolute encoder interface these are serial or parallel interface:
- Parallel: Parallel interfaces commonly use a code called grey code. The disadvantage of this type of data is that it uses a lot of inputs and requires a look up table to obtain the binary data required by the motion controller.
- Serial: There are many serial protocols but a common one is Synchronous Serial Interface (SSI) this is based on the RS422 The serial type requires o'clock pulse to be sent by the controller from which data is clocked out of the encoder and into a register within the motion controller. This type of data is more readily accepted and uses less inputs and therefore most modern motion controllers no longer support parallel absolute encoder inputs.
2. Right is an example of an 8 bit encoder disk.

---
Advantages and disadvantages of rotary absolute encoders
1. It is worthwhile remembering that rotary encoders give the position precisely within one revolution. This may not prove useful, often to obtain higher torque a gearbox is used which may require the motor to do tens of revolutions per millimetre of travel. The problem may well be that during power down the motor is subject to movement and therefore all that is known is the position within one revolution while the actual position data has been lost. For this reason many machines only use incremental encoders. Conventional encoders are robust And tend to be quite noisy immune, the disadvantage with the serial technique is that noise can lead to an erroneous reading which could have serious consequences.

---
Linear absolute encoders
1. Linear absolute encoders are however a totally different matter they are a much more useful device if set properly to not necessary to use home switches or limit switches. Renishaw Absolute linear encoders are available in different ranges. The one shown right has a resolution of 0.274µm and maximum length of 16 metres. There are others in the range this type of encoder such as the LinACE range typically has a resolution of 0.5µm and a maximum movement of 320mm. can be used in many applications such as the Z axis of machine tools hydraulic cylinders etcetera. This particular device is also immune to dirt ingress and is particularly suitable for working in bad environments. This type of linear actuator can be operated at speeds of up to 5m a second. The serial output is available in a number of formats including SSI.
3. The larger formats versions as shown right use the BISS serial format.

---
Input devices
1. Most machines need to use inputs to inform it where a process is. Switches are used for setting an axis in the zero position for example. Below are some examples of some typical devices.
3. Reed switch and magnet:
8. Reed switches are magnetic devices that when a magnet approaches the two contacts are drawn together and a contact is made. These devices do not provide high precision for applications such as home switches, but are cheap and good on devices like pneumatic cylinders. There is some hysteresis which means that the magnet will need to move away a defined distance before switch will drop out. Mechanical switches also suffer bounce.
10. Relay contact:

---
Pulsers
In some applications it is not necessary to use an encoder. Many older machines used to gear tooth or slotted disc with a single channel optical encoder or inductive proximity switch. Many people believe that these provide an encoder output. This is not strictly true because there is only one channel it is not possible to detect the direction of rotation and therefore older machines tend to be subject to overshoot. In applications that use Pulsers for positioning it is necessary to return to the home position after each action this is because of the obvious fact that when the direction is reversed the controller has no means of detecting direction. This type of technology needs to be replaced in modern equipment but is perfectly suitable for controlling speed in applications that are not critical. Techniques varying from optical encoders and revolving metal discs were commonly used in old machines, quite often these days Pulsers are used in devices such as ABS braking. However in old equipment techniques such as rotating magnet and reed switch were not uncommon.

---
Input devices continued
1. Many older machines use relay logic. A relay is a device that uses an electro magnet to cause contacts to come together and make contact. Relays can use reed switches for low signal currents. Relays were often used as input devices but they can be problematic with low currents, this is because the contacts are often coated with anti-arc metals that prevent a plasma. This also makes likelihood of reliable contact at low voltage and current less reliable. Gold flashing offers the best contact material for low signal currents.
3. Inductive Proximity Switches:
8. Proximity switches are very reliable, accurate and are good in many applications. Some of these switches will actually work under liquid. Proximity switches have two many types, these are NPN and PNP. The best wat to think of these is the N means negative so NPN has a negative active output, this means that the device pulls low (to 0 volts). A PNP device when active output positive (normally 24 volts). Inductive proximity switches only work with a metal target they detach the presence of a metal object on the front of the device. They are used by sliding the o9bject in front of the device, they do no work well where the target is drawn away from the device. These devices normally do not need to be debounced and provide good repeatable to within 0.1 mm (typical).