Sefton Adult Learning Service
Industrial and Machine control systems
Presented
By Tony McDonald
Class 3 Inputs and Outputs Continued

---
Input devices
1. Most machines need to use inputs to inform it where a process is. Switches are used for setting an axis in the zero position for example. Below are some examples of some typical devices.
3. Reed switch and magnet:
8. Reed switches are magnetic devices that when a magnet approaches the two contacts are drawn together and a contact is made. These devices do not provide high precision for applications such as home switches, but are cheap and good on devices like pneumatic cylinders. There is some hysteresis which means that the magnet will need to move away a defined distance before switch will drop out. Mechanical switches also suffer bounce.
10. Relay contact:

---
Input devices continued
1. Many older machines use relay logic. A relay is a device that uses an electro magnet to cause contacts to come together and make contact. Relays can use reed switches for low signal currents. Relays were often used as input devices but they can be problematic with low currents, this is because the contacts are often coated with anti-arc metals that prevent a plasma. This also makes likelihood of reliable contact at low voltage and current less reliable. Gold flashing offers the best contact material for low signal currents.
3. Inductive Proximity Switches:
8. Proximity switches are very reliable, accurate and are good in many applications. Some of these switches will actually work under liquid. Proximity switches have two many types, these are NPN and PNP. The best wat to think of these is the N means negative so NPN has a negative active output, this means that the device pulls low (to 0 volts). A PNP device when active output positive (normally 24 volts). Inductive proximity switches only work with a metal target they detach the presence of a metal object on the front of the device. They are used by sliding the o9bject in front of the device, they do no work well where the target is drawn away from the device. These devices normally do not need to be debounced and provide good repeatable to within 0.1 mm (typical).

---
Input devices continued
1. Slotted Opto Switches:
10. Slotted Opto switches are very reliable, and can be very accurate. They work by shinning an infrared light from one side of the switch into a photo device (normally a photo transistor) on the other side. There is a gap in-between the transmitter and receiver and this can be several metres. The device works by using a target that blocks infrared light, when the target is blocking the light the device is in the high impedance state and when the target is not present the light causes the photo transistor to conduct more so it is in the low impedance state. Note sometimes other interface circuitry is needed to convert this signal to a true logic level signal. Since the device is a detector it can be used in either the NPN or PNP mode.

---
Input devices continued
1. Hall effect device:
7. Hall effect devices are available in at least two forms these are analogue and digital. For digital inputs it is better to use a hall effect switch (digital). The device works when a magnet is aligned with the centre of the device and that the polarity is correct (e.g. some need North others South) These devices are very fast and can be used in many applications such as motors. The hall device is normally fixed and the magnet is the moving device. However this magnet can be very small and light.

---
Analogue devices
1. Pressure transducer:
10. Pressure transducers are used to measure pressures, this can be gas or liquid, these devices are reliable but produce and analogue output, sometimes this output can be as low as 20 mV. There are many such devices on the market, including differential devices where the device measures the pressure between the two different ports of the device.
12. Devices tend to be either silicon devices or using a strain gauge and diaphragm plate made from stainless steel or ceramic.

---
Analogue devices
1. Thermocouple:
10. Thermocouples are basically just two wires welded together. There are two junctions on these devices these are the hot junction and the cold junction. The device provides a voltage equivalent to the temperature difference between the hot and cold junctions. This voltage is very low at around about 20uV per degree Celsius. Because the device is differential it needs to be compensated to read ambient temperature, this is called cold junction compensation.

---
Analogue devices
1. Load Cell:
10. Load cells are used to measure weight load or strain. Load cells use a device that is called a strain gauge, these devices use the surface stretch to change their resistance and thereby the voltage when wired in a bridge arrangement.

---
Analogue devices
1. Measurement standards:
3. Some devices or instruments use an analogue output to transmit data to another controller. For example some thermocouple interface devices send the output in either voltage or current modes. These are normally either 0-10 volts +/-10Volts 0-2 volts or in the current mode 0-20 mA or 4 to 20mA.
5. Current is preferred to voltage as constant current output automatically compensate for noise that has been picked up in cables etc.