Sefton Adult Learning Service
Industrial and Machine control systems
Presented
By Tony McDonald
Class 9 software modules for the chop saw program

---
Vectors and Motion
Planning a program, code modules
This section includes modules that you will need to finish your project . We started the course explaining motors, memory, binary, hexadecimal inputs and outputs including air cylinders Now we are going to put them to use.
The machine needs the following sensors assuming that the saw uses two motor controlled axis:
- Home switch for the x axis ( this feeds the material into the saw ).
- Saw home switch. (this is active when the switch is in the up position).
- Material present sensor ( this informs us if material is present ).
There are few outputs needed on this projects these are as a minimum of two.
- Clamp activation.
- Saw blade on.
Let us investigate how we use inputs:
Inputs are arranged in a group normally in byte wide arrangements. Input ports are considered to be volatile that is they prone to change and may have fast moving signals some may exceed 10Kilo hertz. The way volatile ports are read is to copy the port into memory a variable. Ports often appear as memory, this is called memory mapped, older systems used a system which used another instruction system and these ports did not appear on the memory map but on an IO channel. Most ports are dealt with by the operating system (OS) and so reading a port is a process in which the OS returns a variable reflecting the port bits. I MAPO you can read a port in various ways, however most time we are more interested in a single port bit or bits.
Below is some C code to read a port bit, following that is some MAP code.

---
// Read a port bit in the C Programming language
int read_port(int bit)
{
int result;
int compare;
result = get_port();
compare = 1 << bit
result = (result & compare);
return ( result );
}
This will return either 0 or non zero for the value of bit. In the function note
 the use of the & this uses an AND to compare the value of bit and the port bit.
When we and a
Value with another if both bits are logic 1 the result will be one.
After this you still need to use a compare like if.

---
The above code uses a BrancFalse to check a port bit. In the above register 0 is not
tested but input port bit 2 is tested for bring low. If bit 2 is low then the process will
continue on the next line if not the program counter is transferred to the line
labelled by Loop1. Any of the compare instructions can be used
these include IF, BrancFalse, BrancTrue and a do/while.
Note that is this case if the port bit is low an error message will be displayed.
After the user has read the message and pressed a button the next BrancFalse
will cause the program counter to be reloaded to the address of Loop2.

---
1. Outputs
2. There are various ways for changing a output or outputs these are the Output and the ChangeOp. Output can be used to change one or more outputs for example
    1. Output 0	// changes all the outputs to 0 (all off)
    3. The most useful approach is probably the ChangeOp command this allows a single output On or Off. To change an output to on we write a logic 1 to the output.
    4. ChangeOp 8 , 1
    5. This turns output 8 on
        ChangeOp 8 , 0
This turns output 8 off

---
1. Using the data from the operator menu:
2. Most people have used Register 10, for those who have designed a single cutting list menu your data is easy There are various ways for changing a output or outputs these are the Output and the ChangeOp. Output can be used to change one or more outputs for example
    1. Output 0	// changes all the outputs to 0 (all off)
    3. The most useful approach is probably the ChangeOp command this allows a single output On or Off. To change an output to on we write a logic 1 to the output.
    4. ChangeOp 8 , 1
    5. This turns output 8 on
        ChangeOp 8 , 0
This turns output 8 off